## Slide 1: Firewall Training

## Slide 2: Lesson 1 Security Appliance Overview

## Slide 3: What Is a Firewall?
Outside
Network
DMZ
Network
Inside
Network
Internet
A firewall is a system or group of systems that manages access between two or more networks.

## Slide 4: Security Appliances: What Are They?
Deliver enterprise-class security for small-to-medium-sized business and enterprise networks in a modular, purpose-built appliance.
  Proprietary operating system
  Stateful packet inspection
  Proxy Servers
  Packet filtering
  User-based authentication
  Protocol and application inspection
  Modular policy framework
  VPN
  Security contexts (virtual firewalls)
  Stateful failover capabilities
  Transparent firewalls
  Web-based management solutions

## Slide 5: Packet Filtering
Data A B
Data A C
DMZ:
Server B
Inside:
Server C
Host A
AB-Yes
AC-No
Internet
Limits information that is allowed into a network based on the destination and source address

## Slide 6: Proxy Server
Outside
Network
Proxy
Server
Inside
Network
Internet
Requests connections on behalf of a client
the ASA to, on behalf of another device, stop traffic as it's coming in, authenticate its originator at Level 1, and allow all future packets from the same user to cut through at L3.

## Slide 7: Stateful Packet Filtering
172.16.0.50
10.0.0.11
1026
80
49091
Syn
172.16.0.50
192.168.0.20
49769
Syn
1026
80
Source port
Destination address
Source address
Initial sequence no.
Destination port
Flag
Ack
State Table
DMZ:
Server B
Inside:
Server C
Host A
Internet
Limits information that is allowed into a network based not only on the destination and source addresses, but also on the packets state table content
Data HTTP A B

## Slide 8: Stateful Packet Inspection
  The stateful packet inspection algorithm provides stateful connection security.
    It tracks source and destination ports and addresses, TCP sequence numbers, and additional TCP flags.
    It randomizes the initial TCP sequence number of each new connection.
  By default, the stateful packet inspection algorithm allows connections originating from hosts on inside (higher security level) interfaces.
  By default, the stateful packet inspection algorithm drops connection attempts originating from hosts on outside (lower security level) interfaces.
  The stateful packet inspection algorithm supports AAA.

## Slide 9: Application-Aware Inspection
FTP
Server
Client
Control
Port
2008
Data
Port
2010
Data
Port 20
Control
Port
21
Data - Port 2010
Port 2010 OK
Data
  Protocols such as FTP, HTTP, H.323, and SQL*Net need to negotiate connections to dynamically assigned source or destination ports through the firewall.
  Inspects packets above the network layer.
  Securely opens and closes negotiated ports for legitimate client-server connections through the firewall.

## Slide 10: Modular Policy
Headquarters
System Engineer
Site B
Executives
Site C
T1
Internet
SE
exec
S2S
S2S
Internet
Class Map
Traffic Flow
Default
Internet
Systems Engineer
Executives
Site to Site
Policy Map
Services
Inspect
IPS
Police
Priority
Service Policy
Interface/Global
Global
Outside

## Slide 11: Next Generation Firewalls
Identity-Policy Control
URL Filtering
(subscription)
Firepower Analytics & Automation
Advanced Malware
Protection
(subscription)
Intrusion Prevention
(subscription)
Application
Visibility & Control
Network Firewall
Routing | Switching
High Availability
WWW
Cisco Collective Security Intelligence Enabled
Built-in Network Profiling

## Slide 12: Contrast NGFW, NGIPS
NGFW
  Capable of traditional stateful firewall.
  Includes AVC.
Supports identity in policy configuration
  Provides advanced security protection
NGIPS
  Uses pattern matching to detect and drop malicious traffic.
  Deployed on the host (HIPS) or network (NIPS)
  Utilises contextual information to evaluate threat

## Slide 13: Compare NGFW, NGIPS
All require the ability to parse network protocols.
All require security intelligence to keep
up with new threats.
All require adaptation to address the
changing security landscape

## Slide 14: Virtual Private Network
B A N K
Site to Site
Remote Access
IPsec VPN
SSL VPN
Internet
B A N K
Headquarters

## Slide 15: Security Context (Virtual Firewall)
Four Physical Firewalls
One Physical Firewall
Four Virtual Firewalls
Internet
Internet
  Ability to create multiple security contexts within a single security appliance

## Slide 16: Failover Capabilities: Active/Standby, Active/Active, and Stateful Failover
Primary:
Failed Firewall
Secondary:
Active Firewall
Internet
Failover: Active/Standby
Primary:
Failed/Standby
Failover: Active/Active
Secondary:
Active/Active
Internet
Contexts
Failover protects the network if the primary security appliance goes offline..
    Active/standby: Only one unit can be actively processing traffic; the other is hot standby.
    Active/Active: Both units can process traffic and serve as backup units.
Stateful failover maintains the operating state during failover.
2
1
2
1

## Slide 17: Transparent Firewall
192.168.1.2
192.168.1.5
Internet
  Has the ability to deploy a security appliance in a secure bridging mode
  Provides rich L2 through 7 security services as a L2 device

## Slide 18: Web-Based Management Solutions
Adaptive
Security
Device
Manager

## Slide 19: Summary
  A firewall is a system or group of systems that manages access between two or more networks.
  Statefull firewall is a device works most effectively
  Security devices ASA 5510, 5520 targeting the small and medium enterprises.
  The function of security devices can be expanded by the SSMs

## Slide 20: Lesson 2 Getting Started with Security Applicances

## Slide 21
User Interface

## Slide 22: Security Appliance Access Modes
ciscoasa>
ciscoasa#
ciscoasa(config)#
monitor>
A Cisco security appliance has four main administrative access modes:
  Unprivileged
  Privileged
  Configuration
  Monitor

## Slide 23: Access Privileged Mode
ciscoasa> enable
password:
ciscoasa#
enable [priv_level]
ciscoasa>
  Used to control access to the privileged mode
  Enables you to enter other access modes
Internet

## Slide 24: Access Configuration Mode: configure terminal Command
  Used to start configuration mode to enter configuration commands from a terminal
configure terminal
ciscoasa#
ciscoasa> enable
password:
ciscoasa# configure terminal
ciscoasa(config)# exit
ciscoasa# exit
ciscoasa>
exit
ciscoasa#
  Used to exit from an access mode

## Slide 25: help command
ciscoasa > help ?
enable Turn on privileged commands
exit Exit the current command mode
login Log in as a particular user
logout Exit from current user profile to unprivileged mode
perfmon Change or view performance monitoring options
ping Test connectivity from specified interface to an IP address
quit Exit the current command mode
ciscoasa > help enable
USAGE:
enable [<priv_level>]

## Slide 26
File Management

## Slide 27: Viewing and Saving Your Configuration
The following commands enable you to view your configuration:
  Show running-config
  Show startup-config
The following commands enable you to save your configuration:
  copy run start
  write memory
To save configuration changes:
copy run start
running-
config
startup-
config
(saved)
Configuration
Changes

## Slide 28: Clearing Running Configuration
ciscoasa(config)#
clear configure all
  Clears the running configuration
ciscoasa(config)# clear config all
Clear the running configuration:
clear config all
running-
config
(default)
startup-
config

## Slide 29: Clearing Startup Configuration
ciscoasa#
write erase
  Clears the startup configuration
ciscoasa# write erase
Clear the startup configuration:
write erase
running-
config
startup-
config
(default)

## Slide 30: Reload the Configuration: reload Command
  Reboots the security appliance and reloads the configuration
  Allows scheduled reboots
ciscoasa# reload
Proceed with reload?[confirm] y
Rebooting...
reload [at hh:mm [month day | day month]] [cancel] [in [hh:]mm] [max-hold-time [hh:]mm] [noconfirm] [quick] [reason text] [save-config]
ciscoasa#

## Slide 31: File System
Release 7.0
and later
  Software image
  Configuration file
  Private data
  ASDM image
  Backup image*
  Backup configuration file*

## Slide 32: Displaying Stored Files: System and Configuration
  Display the directory contents
ciscoasa#
PIX Security Appliance
flash:
ASA
disk0:
disk1:
ciscoasa# dir
Directory of disk0:/
8 -rw- 8202240 13:37:33 Jul 28 2006 asa721-k8.bin
1264 -rw- 5539756 13:21:13 Jul 28 2006 asdm-521.bin
62947328 bytes total (49152000 bytes free)
dir [/all] [/recursive] [all-filesystems] [disk0: | disk1: | flash: | system:]
Internet

## Slide 33: Security Level Example
Outside Network
GigabitEthernet0/0
Security level 0
Interface name = outside
DMZ Network
GigabitEthernet0/2
Security level 50
Interface name = DMZ
Inside Network
GigabitEthernet0/1
Security level 100
Interface name = inside
g0/0
g0/2
g0/1
Internet

## Slide 34
Examining Security Appliance Status

## Slide 35: show commands
asa1# show interface
Interface GigabitEthernet0/0 "outside", is up, line protocol is up
Detected: Speed 1000 Mbps, Full-duplex
Requested: Auto
MAC address 000b.fcf8.c538, MTU 1500
IP address 192.168.1.2, subnet mask 255.255.255.0
0 packets input, 0 bytes, 0 no buffer
Received 0 broadcasts, 0 runts, 0 giants
0 input errors, 0 CRC, 0 frame, 0 overrun, 0 ignored, 0 abort
0 packets output, 0 bytes, 0 underruns
input queue (curr/max blocks): hardware (0/0) software (0/0)
output queue (curr/max blocks): hardware (0/0) software (0/0)
Received 0 VLAN untagged packets, 0 bytes
Transmitted 0 VLAN untagged packets, 0 bytes
Dropped 0 VLAN untagged packets
asa1# show run interface
. . .
interface GigabitEthernet0/0
speed 1000
duplex full
nameif outside
security-level 0
ip address 192.168.1.2 255.255.255.0
!
interface GigabitEthernet0/1
speed 1000
duplex full
nameif inside
security-level 100
ip address 10.0.1.1 255.255.255.0 . . .
show run interface
show interface

## Slide 36: show memory
asa1# show memory
Free memory: 468962336 bytes (87%)
Used memory: 67908576 bytes (13%)
------------- ----------------
Total memory: 536870912 bytes (100%)
ciscoasa#
show memory

## Slide 37: show cpu usage
asa1# show cpu usage
CPU utilization for 5 seconds = 0%; 1 minute: 0%; 5 minutes: 0%
ciscoasa#
show cpu usage
10.0.1.11
10.0.1.4
Internet

## Slide 38: show version
asa1# show version
Cisco Adaptive Security Appliance Software Version 7.2(1)
Device Manager Version 5.2(1)
Compiled on Wed 31-May-06 14:45 by root
System image file is "disk0:/asa721-k8.bin"
Config file at boot was "startup-config"
ciscoasa up 2 mins 51 secs
Hardware: ASA5520, 512 MB RAM, CPU Pentium 4 Celeron 2000 MHz
Internal ATA Compact Flash, 64MB
BIOS Flash AT49LW080 @ 0xffe00000, 1024KB
. . .

## Slide 39: show ip address
asa1# show ip address
System IP Addresses:
Interface Name IP address Subnet mask Method
GigabitEthernet0/0 outside 192.168.1.2 255.255.255.0 CONFIG
GigabitEthernet0/1 inside 10.0.1.1 255.255.255.0 CONFIG
GigabitEthernet0/2 dmz 172.16.1.1 255.255.255.0 CONFIG
Current IP Addresses:
Interface Name IP address Subnet mask Method
GigabitEthernet0/0 outside 192.168.1.2 255.255.255.0 CONFIG
GigabitEthernet0/1 inside 10.0.1.1 255.255.255.0 CONFIG
GigabitEthernet0/2 dmz 172.16.1.1 255.255.255.0 CONFIG
Internet
192.168.1.0
10.0.1.0
10.1.1.0
172.16.1.0
.2
.1
.1
.1

## Slide 40: show interface
asa1# show interface
Interface GigabitEthernet0/0 "outside", is up, line protocol is up
Hardware is i82546GB rev03, BW 1000 Mbps
Full-Duplex(Full-duplex), 100 Mbps(100 Mbps)
MAC address 0013.c482.2e4c, MTU 1500
IP address 192.168.1.2, subnet mask 255.255.255.0
8 packets input, 1078 bytes, 0 no buffer
Received 8 broadcasts, 0 runts, 0 giants
0 input errors, 0 CRC, 0 frame, 0 overrun, 0 ignored, 0 abort
0 L2 decode drops
0 packets output, 0 bytes, 0 underruns
0 output errors, 0 collisions
0 late collisions, 0 deferred
input queue (curr/max blocks): hardware (8/0) software (0/0)
output queue (curr/max blocks): hardware (0/0) software (0/0)
Traffic Statistics for "outside":
8 packets input, 934 bytes
0 packets output, 0 bytes
8 packets dropped
1 minute input rate 0 pkts/sec, 0 bytes/sec
1 minute output rate 0 pkts/sec, 0 bytes/sec
1 minute drop rate, 0 pkts/sec
5 minute input rate 0 pkts/sec, 0 bytes/sec
5 minute output rate 0 pkts/sec, 0 bytes/sec
5 minute drop rate, 0 pkts/sec

## Slide 41: show nameif
asa1# show nameif
Interface Name Security
GigabitEthernet0/0 outside 0
GigabitEthernet0/1 inside 100
GigabitEthernet0/2 dmz 50
GigabitEthernet0/0
Interface name = outside
Security level = 0
GigabitEthernet0/2
Interface name = dmz
Security level = 50
GigabitEthernet0/1
Interface name = inside
Security level = 100
g0/0
g0/2
g0/1
Internet

## Slide 42: show run nat
asa1# show run nat
nat (inside) 1 10.0.1.0 255.255.255.0 0 0
  Displays a single host or range of hosts to be translated
ciscoasa#
show run nat
10.0.1.11
10.0.1.4
10.0.1.X
X.X.X.X
NAT
Internet

## Slide 43: show run global
asa1# show run global
global (outside) 1 192.168.1.20-192.168.1.254 netmask 255.255.255.0
  Displays the pool of mapped addresses
ciscoasa#
show run global
Mapped Pool
192.168.1.20-192.168.1.254
10.0.1.11
10.0.1.4
10.0.1.X
Internet

## Slide 44: show xlate
asa1# show xlate
1 in use, 1 most used
Global 192.168.1.20 Local 10.0.1.11
  Displays the contents of the translation slots
ciscoasa#
show xlate
192.168.1.20
10.0.1.11
10.0.1.4
10.0.1.11
Inside
local
Outside
mapped pool
10.0.1.11
192.168.1.20
Xlate Table
Internet

## Slide 45: show route
asa1(config)# show route
S 0.0.0.0 0.0.0.0 [1/0] via 192.168.1.1, outside
C 10.0.1.0 255.255.255.0 is directly connected, inside
C* 127.0.0.0 255.255.0.0 is directly connected, cplane
C 172.16.1.0 255.255.255.0 is directly connected, dmz
C 192.168.1.0 255.255.255.0 is directly connected, outside
g0/0
g0/2
g0/1
Internet
10.0.1.0
192.168.1.0
.1
172.16.1.0
  Displays the contents of the routing table
ciscoasa#
show route [interface_name [ip_address [netmask [static]]]]

## Slide 46: ping Command
  Determines whether other devices are visible from the security appliance
asa1# ping 10.0.1.11
Sending 5, 100-byte ICMP Echos to 10.0.1.11, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 10/12/20 ms
ping [if_name] host [data pattern] [repeat count] [size bytes] [timeout seconds] [validate]
ciscoasa#
10.0.1.11
10.0.1.4
Internet

## Slide 47: traceroute
asa1#traceroute 172.26.26.20
traceroute {destination_ip | hostname} [source source_ip | source-interface] [numeric] [timeout timeout_value] [probe probe_num] [ttl min_ttl max_ttl] [port port_value] [use-icmp]
ciscoasa#
  Determines the route packets will take to their destination
Internet
example.com

## Slide 48
Basic Security Appliance Configuration

## Slide 49: Basic CLI Commands
  hostname
  interface
    nameif
    ip address
    security-level
    speed
    duplex
    no shutdown
  nat-control
  nat
  global
  route
g0/0
g0/2
g0/1
Internet

## Slide 50: Assigning a Hostname to Security Appliance: Changing the CLI Prompt
  Changes the hostname in the security appliance CLI prompt
ciscoasa(config)#
ciscoasa(config)# hostname asa1 asa1(config)#
hostname newname
New York ( asa1)
Server
Boston
(asa2)
Server
Server
Dallas
(asa3)
Internet

## Slide 51: interface Command and Subcommands
interface {physical_interface[.subinterface] | mapped_name}
ciscoasa(config)#
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)#
  Enters configuration mode for the interface you specify
GigabitEthernet0/0
GigabitEthernet0/2
GigabitEthernet0/1
g0/0
g0/2
g0/1
Internet

## Slide 52: Assign an Interface Name: nameif Subcommand
nameif if_name
ciscoasa(config-if)#
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# nameif outside
  Assigns a name to an interface on the security appliance.
GigabitEthernet0/2
Interface name = dmz
GigabitEthernet0/0
Interface name = outside
GigabitEthernet0/1
Interface name = inside
g0/0
g0/2
g0/1
Internet

## Slide 53: Assign Interface IP Address: ip address Subcommand
ip address ip_address [mask] [standby ip_address]
ciscoasa(config-if)#
  Assigns an IP address to each interface
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# nameif outside
asa1(config-if)# ip address 192.168.1.2 255.255.255.0
GigabitEthernet0/0
Interface name = outside
IP address = 192.168.1.2
g0/0
g0/2
g0/1
Internet

## Slide 54: DHCP-Assigned Address
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# nameif outside
asa1(config-if)# ip address dhcp
ciscoasa(config-if)#
ip address dhcp [setroute]
  Enables the DHCP client feature on the outside interface
GigabitEthernet0/0
Interface name = outside
IP address = dhcp
g0/0
DHCP
Assigned
Internet

## Slide 55: Assign a Security Level: security-level Subcommands
security-level number
ciscoasa(config-if)#
  Assigns a security level to the interface
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# nameif outside
asa1(config-if)# ip address 192.168.1.2
asa1(config-if)# security-level 0
GigabitEthernet0/0
Interface name = outside
IP address = 192.168.1.2
Security level = 0
g0/0
g0/2
g0/1
Internet

## Slide 56: Interfaces with Same Security Level: same-security-traffic Command
  Enables communication between interfaces with the same security level or allows traffic to enter and exit the same interface
ciscoasa(config)#
asa1(config)# same-security-traffic permit inter-interface
same-security-traffic permit {inter-interface | intra-interface}
DMZ Network
GigabitEthernet0/2
Security level 100
Interface name = dmz
g0/0
g0/2
g0/1
Internet
Inside Network
GigabitEthernet0/1
Security level 100
Interface name = inside

## Slide 57: Assign an Interface Speed and Duplex: speed and duplex SubCommands
speed {10 | 100 | 1000 | auto | nonegotiate}
duplex {auto | full | half}
  Enable the interface speed and duplex
ciscoasa(config-if)#
GigabitEthernet0/0
Speed =1000
Duplex = full
g0/0
g0/2
g0/1
Internet
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# nameif outside
asa1(config-if)# ip address 192.168.1.2
asa1(config-if)# security-level 0
asa1(config-if)# speed 1000
asa1(config-if)# duplex full

## Slide 58: ASA Management Interface
management-only
ciscoasa(config-if)#
  Disables management-only mode (for ASA 5520, 5540 and 5550)
asa1(config)# interface management0/0
asa1(config-if)# no management-only
no management-only
  Configures an interface to accept management traffic only
  Disables management-only mode
Management0/0
Management only = no
g0/0
g0/2
g0/1
Internet
m0/0

## Slide 59: Enabling and Disabling Interfaces: shutdown Subcommand
  Disables management-only mode (for ASA 5520, 5540 and 5550)
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# no shutdown
shutdown
  Disables an interface
  no shutdown = enabled
ciscoasa(config-if)#
GigabitEthernet0/0
Enabled
g0/0
g0/2
g0/1
Internet

## Slide 60: Network Address Translation
Inside
Local
Outside
Mapped Pool
10.0.0.11
192.168.0.20
10.0.0.11
10.0.0.4
Translation Table
10.0.0.11
192.168.0.20
192.168.10 .11
NAT
Internet

## Slide 61: Enable NAT Control
asa1(config)# nat-control
Enable or disable NAT configuration requirement
Inside
Local
Outside
Mapped Pool
10.0.0.11
192.168.0.20
10.0.0.11
10.0.0.4
Translation Table
10.0.0.11
192.168.0.20
200.200.200.11
NAT
Internet

## Slide 62: nat command
nat (if_name) nat_id address [netmask] [dns]
ciscoasa(config)#
  Enables IP address translation
asa1(config)# nat (inside) 1 0.0.0.0 0.0.0.0
10.0.1.11
10.0.1.4
10.0.1.11
X.X.X.X
NAT
Internet

## Slide 63: global command
  Works with the nat command to assign a registered or public IP address to an internal host when accessing the outside through the firewall, for example, 192.168.0.20-192.168.0.254
asa1(config)# nat (inside) 1 0.0.0.0 0.0.0.0
asa1(config)# global (outside) 1 192.168.1.20-192.168.1.254
  global(if_name) nat_id {mapped_ip[-mapped_ip] [netmask mapped_mask]} | interface
ciscoasa(config)#
10.0.1.11
10.0.1.4
10.0.1.11
192.168.1.20
NAT
Internet

## Slide 64: Configure a Static Route: route Command
route if_name ip_address netmask gateway_ip [metric]
ciscoasa(config)#
  Defines a static or default route for an interface
asa1(config)# route outside 0.0.0.0 0.0.0.0 192.168.1.1 1
asa1(config)# route inside 10.1.1.0 255.255.255.0 10.0.1.102 1
192.168.1.1
10.1.1.11
10.1.1.4
Default Route
10.0.1.102
Static Route
Internet

## Slide 65: Host Name-to-IP-Address Mapping: name Command
asa1(config)# names
asa1(config)# name 172.16.1.2 bastionhost
asa1(config)# name 10.0.1.11 insidehost
  Configures a list of name-to-IP-address mappings on the security appliance
name ip_address name
ciscoasa(config)#
.2
.1
10.0.1.0
.1
Internet
“bastionhost”
172.16.1.2
172.16.1.0
.11
“insidehost”
10.0.1.11

## Slide 66: Configuration Example
  asa1(config)# write terminal
  . . .
  interface GigabitEthernet0/0
  speed 1000
  duplex full
  nameif outside
  security-level 0
  ip address 192.168.1.2 255.255.255.0
  interface GigabitEthernet0/1
  speed 1000
  duplex full
  nameif inside
  security-level 100
  ip address 10.0.1.1 255.255.255.0 . . .
GigabitEthernet0/0
Interface name = outside
Security level = 0
IP address = 192.168.1.2
GigabitEthernet0/1
Interface name = inside
Security level = 100
IP address = 10.0.1.1
172.16.1.0
.1
10.0.1.0
.1
192.168.1.0
.2
10.1.1.0
.1
Internet

## Slide 67: Configuration Example
  interface GigabitEthernet0/2
  nameif dmz
  security-level 50
  speed 1000
  duplex full
  ip address 172.16.1.1 255.255.255.0
  passwd 2KFQnbNIdI.2KYOU encrypted
  hostname asa1
  names
  name 172.16.1.2 bastionhost
  name 10.1.1.11 insidehost
172.16.1.0
.1
10.0.1.0
.1
192.168.1.0
.2
10.1.1.0
.1
GigabitEthernet0/2
Interface name = dmz
Security level = 50
IP address = 172.16.1.1
“insidehost”
10.1.1.11
“bastionhost”
172.16.1.2
Internet

## Slide 68: Configuration Example
  nat-control
  nat (inside) 1 0.0.0.0 0.0.0.0 0 0
  global (outside) 1 192.168.1.20-192.168.1.254
  route outside 0.0.0.0 0.0.0.0 192.168.1.1 1
  route inside 10.1.1.0 255.255.255.0 10.0.1.102 1
10.0.0.0
Mapped Pool
192.168.1.20 - 254
172.16.1.0
.2
.1
.102
“insidehost”
10.1.1.11
“bastionhost”
172.16.1.2
10.0.1.0
.1
192.168.1.0
.2
.1
10.1.1.0
.1
Default Route
Static Route
Internet

## Slide 69: Summary
  Four main administrative access modes: unprivileged, privileged, configuration, and monitor.
  Two configuration memories in the security appliances: running configuration and startup configuration.
  The show running-config displays the current configuration in the RAM on the terminal.
  You can use the copy run start or the write memory command to save the current running configuration.
  Interfaces with a higher security level can access interfaces with a lower security level, but interfaces with a lower security level cannot access interfaces with a higher security level unless given permission.
  The basic commands that are necessary to configure Cisco security appliances are the following: interface, nat, global, and route.
  The nat and global commands work together to translate IP addresses.

## Slide 70: Lesson 3 Managing the Security Appliance

## Slide 71
Managing System Access

## Slide 72: Configuring Telnet Access to the Security Appliance Console
telnet {{hostname | IP_address mask interface_name} | {IPv6_address interface_name} | {timeout number}}
ciscoasa(config)#
asa1(config)# telnet 10.0.0.11 255.255.255.255 inside
asa1(config)# telnet timeout 15
asa1(config)# passwd telnetpass
  Enables you to specify which hosts can access the security appliance console with Telnet and set the maximum time a console Telnet session can be idle before being logged off by the security appliance
  Sets the password for Telnet access to set the security appliance
passwd password [encrypted]
ciscoasa(config)#
10.0.0.11
Telnet
Internet

## Slide 73: Viewing and Disabling Telnet
kill telnet_id
ciscoasa#
  Terminates a Telnet session
  Enables you to view which IP addresses are currently accessing the security appliance console via Telnet
who [local_ip]
ciscoasa#
  Removes the Telnet connection and the idle timeout from the configuration
clear configure telnet
ciscoasa(config)#
  Displays IP addresses permitted to access the security appliance via Telnet
show running-config telnet [timeout]
ciscoasa#

## Slide 74: SSH Connections to the Security Appliance
SSH connections to the security appliance:
  Provide secure remote access
  Provide strong authentication and encryption
  Require RSA key pairs for the security appliance
  Require 3DES/AES or DES activation keys
  Allow up to five SSH clients to simultaneously access the security appliance console
  Use the Telnet password for local authentication

## Slide 75: Configuring SSH Access to the Security Appliance Console
crypto key zeroize {rsa | dsa} [label key-pair-label] [default] [noconfirm]
  Removes any previously generated RSA keys
ciscoasa(config)#
  Saves the CA state
write memory
ciscoasa(config)#
  Configures the domain name
domain-name name
ciscoasa(config)#
  Generates an RSA key pair
crypto key generate rsa [usage-keys | general-keys] [label key-pair-label] [modulus size] [noconfirm]
ciscoasa(config)#
  Specifies the host or network authorized to initiate an SSH connection
ssh {ip_address mask | ipv6_address/prefix} interface
ciscoasa(config)#
  Specifies how long a session can be idle before being disconnected
ssh timeout number
ciscoasa(config)#

## Slide 76: Connecting to the Security Appliance with an SSH Client
asa1(config)# crypto key zeroize rsa
asa1(config)# write memory
asa1(config)# domain-name cisco.com
asa1(config)# crypto key generate rsa modulus 1024
asa1(config)# write memory
asa1(config)# ssh 172.26.26.50 255.255.255.255 outside
asa1(config)# ssh timeout 30
172.26.26.50
SSH
username: pix
password: telnetpassword
Internet

## Slide 77
Managing Configurations

## Slide 78: Viewing Directory Contents
  Displays the directory contents
dir [/all] [/recursive] [all-filesystems | [disk0: | disk1: | flash: | system:] path]
ciscoasa#
asa1# dir
Directory of disk0:/
4346 -rw- 8202240 15:01:10 Oct 19 2006 asa721-k8.bin
6349 -rw- 5539756 15:30:39 Oct 19 2006 asdm521.bin
7705 -rw- 3334 07:03:57 Oct 22 2006 old_running.cfg
62947328 bytes total (29495296 bytes free)
10.0.0.3
10.0.0.11
192.168.0.0
dir
Internet
You can use the pwd command to display the current working directory.

## Slide 79: Copying Files
  Copies a file from one location to another
copy [/noconfirm | /pcap] {url | running-config | startup-config} {running-config | startup-config | url}
ciscoasa#
asa1# copy disk0:MYCONTEXT.cfg startup-config
10.0.0.3
10.0.0.11
192.168.0.0
copy
Internet
  Copies the file MYCONTEXT.cfg from disk0 to the startup configuration

## Slide 80: Downloading and Backing Up Configuration Files Example
ciscoasa#
ciscoasa#
  Copies the configuration file from an FTP server
  Copies the configuration file to an FTP server
10.0.0.3
10.0.0.11
192.168.0.0
FTP server
config
Internet
copy ftp: startup-config
copy running-config ftp:

## Slide 81: Summary
  SSH provides secure remote management of the security appliance.
  TFTP is used to upgrade the software image on security appliances.
  You can enable Telnet to the security appliance on all interfaces.
  .

## Slide 82: Lesson 4 Access Control List

## Slide 83: Security Appliance ACL Configuration
Outside
Inside
ACL for
Inbound Access
ACL for
Outbound Access
No ACL
- Outbound permitted by default
- Inbound denied by default
Security appliance configuration philosophy is interface-based.
  Interface ACL permits and denies the initial incoming and outgoing packets on that interface.
  An ACL must describe only the initial packet of the application; return traffic does not need to be described.
  If no ACL is attached to an interface:
    The outbound packet is permitted by default.
    The inbound packet is denied by default.
Internet

## Slide 84: Inbound Traffic to DMZ Web Server
There is no ACL, so by default, inbound access is denied. To permit inbound traffic, complete the following steps:
  Configure a static translation for the web server address
  Configure an inbound ACL
  Apply the ACL to the outside interface
192.168.1.0
10.0.1.0
Public Web
Server
DMZ
Inside
Outside
.2
.1
Inbound
X
Internet

## Slide 85: Create a Static Translation for Web Server
192.168.1.0
10.0.1.0
Public Web
Server
DMZ
Inside
Outside
.2
.1
192.168.1.9
172.16.1.2
  Maps an inside private address to an outside public address
asa1(config)# static (DMZ,outside) 192.168.1.9 172.16.1.2 0 0
Internet

## Slide 86: access-list
  Permits outside HTTP traffic to access the public web server
asa1(config)# access-list ACLOUT permit tcp any host 192.168.1.9 eq www
ciscoasa(config)#
  access-list id [line line-number] [extended] {deny | permit} {protocol | object-group protocol_obj_grp_id}{host sip | sip smask | interface ifc_name | object-group network_obj_grp_id | any} [operator port [port] | object-group service_obj_grp_id] {host dip | dip dmask | interface ifc_name | object-group network_obj_grp_id | any} [operator port [port] | object-group service_obj_grp_id | object-group icmp_type_obj_group_id] [log [[level] [interval secs] | disable | default]] [inactive | time-range time_range_name]
192.168.1.0
10.0.1.0
Public Web Server
DMZ
Inside
Outside
.2
.1
192.168.1.9
172.16.1.2
Permit
Inbound
HTTP
Internet

## Slide 87: access-group
192.168.1.0
10.0.1.0
Public Web
Server
DMZ
Inside
Outside
.2
.1
  Applies an ACL to an interface
asa1(config)# access-group ACLOUT in interface outside
Apply ACL
to interface
ciscoasa(config)#
access-group access-list {in | out} interface interface_name [per-user-override]
Internet

## Slide 88: show access-list Command
asa1(config)# show access-list
access-list cached ACL log flows: total 0, denied 0 (deny-flow-max 4096)
alert-interval 300
access-list ACLOUT; 4 elements
access-list ACLOUT line 1 extended permit tcp 192.168.6.0 255.255.255.0 host 192.168.1.11 eq www (hitcnt=4)0x984ebd70
access-list ACLOUT line 2 extended permit tcp host 192.168.6.10 host 192.168.1.11 eq ftp (hitcnt=1) 0x53490ecd
access-list ACLOUT line 3 extended permit tcp any host 192.168.1.9 eq www (hitcnt=8) 0x83af39ca
access-list ACLOUT line 4 extended deny ip any any (hitcnt=4) 0x2ca30385
access-list ICMPDMZ; 1 elements
access-list ICMPDMZ line 1 extended permit icmp host bastionhost any echo-reply
ICMPDMZ
ACLIN
ACLOUT
192.168.1.0
192.168.6.10
Internet

## Slide 89: clear access-list counters
asa1(config)# clear access-list ACLOUT counters
asa1(config)# show access-list
access-list cached ACL log flows: total 0, denied 0 (deny-flow-max 4096)
alert-interval 300
access-list ACLOUT; 4 elements
access-list ACLOUT line 1 extended permit tcp 192.168.6.0 255.255.255.0 host 192.168.1.11 eq www (hitcnt=0) 0x984ebd70
access-list ACLOUT line 2 extended permit tcp host 192.168.6.10 host 192.168.1.11 eq ftp (hitcnt=0) 0x53490ecd
access-list ACLOUT line 3 extended permit tcp any host 192.168.1.9 eq www (hitcnt=0) 0x83af39ca
access-list ACLOUT line 4 extended deny ip any any (hitcnt=0) 0x2ca30385
Internet
192.168.6.10
Web Server
172.16.1.2
192.168.1.9
ACLIN
ACLOUT

## Slide 90: ACL Logging
  Enables the logging option for inbound ICMP to 192.168.1.11
asa1(config)# access-list OUTSIDE-ACL permit icmp any host 192.168.1.11 log 7 interval 600
ciscoasa(config)#
ACL Syslog
Messages
  access-list id [line line-number] [extended] {deny | permit} {protocol | object-group protocol_obj_grp_id}{host sip | sip smask | interface ifc_name | object-group network_obj_grp_id | any} [operator port [port] | object-group service_obj_grp_id] {host dip | dip dmask | interface ifc_name | object-group network_obj_grp_id | any} [operator port [port] | object-group service_obj_grp_id | object-group icmp_type_obj_group_id] [log [[level] [interval secs] | disable | default]] [inactive | time-range time_range_name]
Internet
Syslog
Server

## Slide 91: ACL Comments
asa1(config)# access-list ACLOUT line 2 remark WebMailA access-list
  Inserts ACL comment
ciscoasa(config)#
  access-list id [line line-number] remark text
asa1(config)# show access-list
access-list cached ACL log flows: total 0, denied 0 (deny-flow-max 4096) alert-interval 300
access-list ACLOUT; 6 elements
access-list ACLOUT line 1 extended permit tcp any host 192.168.1.7 eq www (hitcnt=0) 0x3df6ed1e
access-list ACLOUT line 2 remark WebMailA access-list
access-list ACLOUT line 3 extended permit tcp any host 192.168.1.8 eq www (hitcnt=0) 0xd5383eba
access-list ACLOUT line 4 extended permit tcp any host 192.168.1.9 eq www (hitcnt=0)0x2c4288ad
access-list ACLOUT line 5 extended permit tcp any host 192.168.1.10 eq www (hitcnt=0) 0xb70c935b
access-list ACLOUT line 6 extended permit tcp any host 192.168.1.11 eq www (hitcnt=0) 0x8b43382e
former line 2

## Slide 92: Inbound HTTP Access Solution
  Permits outside HTTP traffic to access the public web server
asa1(config)# static (DMZ,outside) 192.168.1.9 172.16.1.2 0 0
asa1(config)# access-list ACLOUT permit tcp any host 192.168.1.9 eq www
asa1(config)# access-group ACLOUT in interface outside
192.168.1.0
10.0.1.0
Public Web
Server
DMZ
Inside
Outside
.2
.1
192.168.1.9
172.16.1.2
Inbound
Internet

## Slide 93: icmp Command
  Enables or disables pinging to an interface
asa1(config)# icmp permit any echo-reply outside
asa1(config)# icmp permit any unreachable outside
ciscoasa(config)#
  icmp {permit | deny} {host sip | sip smask | any} [icmp-type] if_name
Outside
Inside
ICMP Echo
ICMP Unreachable
X
  Permits all unreachable messages at the outside interface and denies all ping requests at the outside interface
Internet

## Slide 94: Summary
  ACLs enable you to determine which systems can establish connections through your security appliance.
  With ICMP ACLs, you can disable pinging to a security appliance interface so that your security appliance cannot be detected on your network.
  .

## Slide 95: Lesson 5 Adaptive Security Device Manager

## Slide 96
ASDM Overview and Operating Requirements

## Slide 97: What Is ASDM?
ASDM is a browser-based configuration tool designed to help configure and monitor your security appliance.
Internet
SSL Secure Tunnel

## Slide 98: ASDM Browser Requirements
To access ASDM from a browser, the following requirements must be met:
  JavaScript and Java must be enabled on the computer where the browser resides.
  SSL must be enabled in the browser.
  Popup blockers may prevent ASDM from starting.

## Slide 99: Configure the Security Appliance to Use ASDM
Before you can use ASDM, you need to enter the following information on the security appliance via a console terminal:
  Time
  Inside IP address
  Inside network mask
  Host name
  Domain name
  Enable the HTTP server on the security appliance
  IP addresses of hosts authorized to access HTTP server
  If more than one ASDM image is stored in the flash memory of your security appliance, also specify the ASDM image to be used.